O-Frame Application Paper 40-180 gsm

Paper Machine Manufacturing for Paper from recycled materials.

Measurement Values : 1) Basis Weight and 2) Moisture in scanning Mode dividing the web in 128 Profile Data Segments (Cross-Direction), 3) Thick- Stockflow- and 4) Consistency- Measurement (0.1-3% Bone Dry).

Controls : 1) Weight via Thickstock,2) Moisture over Steam and 3) Consistency control.

Technical Data

Basis Weight Measuring Head : Kr-85, 200 mCi

Moisture Measuring Head : Infrared Radiation

Machine Speed : up to 800 m/min

Ambient Conditions

Harsh industrial Enviroment, dusty, Ambient Temperature up to 50 oC

Configuration

Scanning Frame : O-Frame Constuction (4 m Width), automatic scanning between Photocells

System : Main Enclosure (IP54), industrial PC, Printer, Control Valve, Communication ProfiBus-DP